## Slide 1: Background
The Poisson—Boltzmann equation must be solved many times during the solving procedure for self-consistent field equations
For the counterion-only system, numerically solving the PB equation is difficult due to the length scale of the decay.
Key characteristics of PB equation
  Highly non-linear
  One boundary corresponds to charged surface, while other corresponds to charge neutrality of system
  Can be numerically solved using NBC—NBC or NBC—DBC (due to compatibility condition/charge neutrality)

## Slide 2: Previous attempts (1 of 3)
Neumann – Dirichlet
Good for 1 uC/cm2, but cannot provide natural boundary for higher surface charge densities even for very high N

## Slide 3: Previous attempts (2 of 3)
Neumann – (D) – Neumann
Neumann on both sides but choose an arbitrary point to set the value of
(Numerically ill-conditioned, but some stackoverflow comments recommended it for similar problems)
Visually okay, but when implemented into full SCFT, very wrong results (not shown)
−5e-20 C/nm2
−10e-20 C/nm2
−20e-20 C/nm2

## Slide 4: Previous attempts (3 of 3)
“Heat” equation
Neumann on both sides but iterate until “steady state”
Natural boundary condition not met for any mix of numerical conditions

## Slide 5: Non-uniform grid
So far, all uniform grid (space between points equal along line) finite difference
However, solution changes drastically at one interface and slowly at another (log function)
Finite difference is amenable to grid stretching, but must follow some rules
  Mapping needs to be 1-to-1 (easy to accomplish)
  Stretching must be smooth and continuous (adds some limitations)
  For numerical accuracy, stretching function should have low slope when solution high slope (requires some expectation of solution) and vice versa
For the remaining slides:
m = 0.08, D = 0.5
Can do more in-depth explanations later
Fine grid
Coarse grid
Fine grid at one boundary, coarse at another

## Slide 6: Examples
N = 50
N = 100
N = 250
N = 500
N = 1000
Vertical lines: grid points (like a number line)
Transition between coarse grid and fine grid occurs at the “knee” (red)
  Fraction of points on either side of the knee is the same as N increases
Allows for accurate solution of highly changing potential at right boundary and gradual decay at left boundary

## Slide 7: Comparison with analytical results
Dotted:
Infinite boundary condition, log-divergence
Srinivasan et al. Part I. 2024. Langmuir
Note: midpoint concentration can be calculated analytically but wasn’t quite right. In plots, used midpoint concentration obtained with N = 10,000
Dashed:
Finite boundary condition
Solid: numerical solution using N=5000 points
Colors: Surface charge densities in uC/cm2

## Slide 8: Effect of number of grid points (N)
N = 50
N = 100
N = 250
N = 500
N = 1000
Transition knee in red (z ~ 90)
Analytical:
Natural boundary condition met; for higher surface charge densities, more points needed (can also change mapping function but keeping the same for simplicity)

## Slide 9: Effect of domain size, modifying left grid
L = 100
(N=1000)
L = 200
(N=1471)
L = 500
(N=2884)
Original
Extend left (evenly)
L = 50
(N=764)
Chop from left
s = −20e-20

## Slide 10: Effect of domain size, modifying right grid
L = 100
(N=1000)
L = 101
(N=1051)
L = 110
(N=1508)
Original
Extend right (evenly)
L = 95
(N=746)
Chop from right
s = −20e-20

## Slide 11: Addition of homogeneous background charge (z > 95)
s = −1e-20
s = +1e-20
Homo charge
s = −5e-20
s = +5e-20
Homo charge
s = −10e-20
s = +10e-20
Homo charge
Homogeneous charge negative for (z>95), colors indicate different charge densities

## Slide 12: Next steps
Map this grid onto the computational grid used in SCFT
Run SCFT
Get morphologies